## Slide 1: Chapter 1
The Logic of Compound Statements

## Slide 2: Section 1.5
Number Systems and Circuits for Addition
Karnaugh Maps

## Slide 3: Decimal Representation
Recall decimal numbers (base 10) can be described as a number sentence.
  Decimal: 6,145 == 6x1000 + 1x100 + 4x10 + 5
  6x103 + 1x102 + 4x101 + 5x100
  Decimal: 7,000 == 7x1000 + 0x100 + 0x10 + 0
  7x103 + 0x102 + 0x101 + 0x100

## Slide 4: Binary Representation
Binary numbers (base 2) are sequence of {0,1}digits. The value of the number depends on it’s location in the sequence.
  Binary: 1101 => 1x8 + 1x4 + 0x2 + 1
  1x23 + 1x22 + 1x21 + 1x20
  = (decimal) 8+4+0+1 = 1310
  Binary: 10101 => 1x16 + 0x8 + 1x4 + 0x2 + 1
  1x24 + 0x23 + 1x22 + 1x21 + 1x20
  = (decimal) 16+0+4+0+1 = 2110

## Slide 5: Converting Binary to Decimal
Converting from binary to decimal is performed by expanding the binary to a number sentence and summing over the number sentence.
  Example:
    1101012 = 1x25 + 1x24 + 0x23 + 1x22 + 0x21 + 1x20 = 5310

## Slide 6: Converting Decimal to Binary
Convert decimal to binary using the repeated division method as follows. The divisor (bottom number) is the base that the decimal is being converted to.
  Example: Convert 5010 to binary
  5010 = 1100102

## Slide 7: Example
Convert 20910 to binary
Answer: 11010001

## Slide 8: Binary Addition
Binary addition is performed in the same manner as decimal addition.
When and how do you perform a carry?
  Carry is dependent on the base. Sum greater than the (base – 1) results in a carry.
  Example:
    12 + 02 = 1 (no carry)
    02 + 12 = 1 (no carry)
    12 + 12 = 102 (carry)

## Slide 9: Examples

## Slide 10: Binary Subtraction
Binary subtraction is performed in the same manner as decimal subtraction.
When and how do you perform a borrow?
  Borrow is dependent on the base. In decimal you borrow a 10’s value from the adjoining digit, however, in binary you borrow a 102 (210).
  Example:
    12 - 02 = 1 (no borrow)
    12 - 12 = 0 (no borrow)
    102 - 12 = 012 (borrow from 2’s position)
    210 – 110 = 110 (check)

## Slide 11: Examples

## Slide 12: Circuits for Addition
Addition requires two inputs (P, Q) and two outputs (Carry, Sum).
Input/output table can be constructed to show the relationship of P,Q to Carry and P,Q to Sum.

## Slide 13: Addition Circuits Half-Adder

## Slide 14: Addition Circuits Full-Adder
A full adder requires three inputs, (P, Q) and a carry in (R).
Notes: Use canonical form to create circuit

## Slide 15: Addition Circuits Full-Adder
Full-adder can be constructed from multiple half-adders.
Notes: Use canonical form to create circuit

## Slide 16: Addition Circuits Full-Adder
Full-adder can be constructed from two half-adders.
Notes: Use canonical form to create circuit

## Slide 17: Unsigned Integers
Non-positional notation
  could represent a number (“5”) with a string of ones (“11111”)
  problems?
Weighted positional notation
  like decimal numbers: “329”
  “3” is worth 300, because of its position, while “9” is only worth 9
329
102
101
100
101
22
21
20
3x100 + 2x10 + 9x1 = 329
1x4 + 0x2 + 1x1 = 5
most
significant
least
significant

## Slide 18: Unsigned Integers (cont.)
An n-bit unsigned integer represents 2n values: from 0 to 2n-1.
22 | 21 | 20 | 
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 2
0 | 1 | 1 | 3
1 | 0 | 0 | 4
1 | 0 | 1 | 5
1 | 1 | 0 | 6
1 | 1 | 1 | 7

## Slide 19: Signed Integers
With n bits, we have 2n distinct values.
  assign about half to positive integers (1 through 2n-1) and about half to negative (- 2n-1 through -1)
  that leaves two values: one for 0, and one extra
Positive integers
  just like unsigned – zero in most significant (MS) bit 00101 = 5
Negative integers
  sign-magnitude – set MS bit to show negative, other bits are the same as unsigned 10101 = -5
  one’s complement – flip every bit to represent negative 11010 = -5
  in either case, MS bit indicates sign: 0=positive, 1=negative

## Slide 20: Two’s Complement
Problems with sign-magnitude and 1’s complement
  two representations of zero (+0 and –0)
  arithmetic circuits are complex
    How to add two sign-magnitude numbers?
      e.g., try 2 + (-3)
    How to add to one’s complement numbers?
      e.g., try 4 + (-3)
Two’s complement representation developed to make circuits easy for arithmetic.
  for each positive number (X), assign value to its negative (-X), such that X + (-X) = 0 with “normal” addition, ignoring carry out
00101 (5) 01001 (9)
+ 11011 (-5) + (-9)
00000 (0) 00000 (0)

## Slide 21: Two’s Complement Representation
If number is positive or zero,
  normal binary representation, zeroes in upper bits if required.
If number is negative,
  start with positive number
  flip every bit (i.e., take the one’s complement)
  then add one
00101 (5) 01001 (9)
11010 (1’s comp) (1’s comp)
+ 1 + 1
11011 (-5) (-9)

## Slide 22: Two’s Complement Shortcut
To take the two’s complement of a number:
  copy bits from right to left until (and including) the first “1”
  flip remaining bits to the left
011010000 011010000
100101111 (1’s comp)
+ 1
100110000 100110000
(copy)
(flip)

## Slide 23: Two’s Complement Signed Integers
MS bit is sign bit – it has weight –2n-1.
Range of an n-bit number: -2n-1 through 2n-1 – 1.
  The most negative number (-2n-1) has no positive counterpart.
-23 | 22 | 21 | 20 | 
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
-23 | 22 | 21 | 20 | 
1 | 0 | 0 | 0 | -8
1 | 0 | 0 | 1 | -7
1 | 0 | 1 | 0 | -6
1 | 0 | 1 | 1 | -5
1 | 1 | 0 | 0 | -4
1 | 1 | 0 | 1 | -3
1 | 1 | 1 | 0 | -2
1 | 1 | 1 | 1 | -1

## Slide 24: Converting Binary (2’s C) to Decimal
If leading bit is one, take two’s complement to get a positive number.
Add powers of 2 that have “1” in the corresponding bit positions.
If original number was negative, add a minus sign.
n | 2n
0 | 1
1 | 2
2 | 4
3 | 8
4 | 16
5 | 32
6 | 64
7 | 128
8 | 256
9 | 512
10 | 1024
X = 011010002
= 26+25+23 = 64+32+8
= 10410
Assuming 8-bit 2’s complement numbers.

## Slide 25: More Examples
n | 2n
0 | 1
1 | 2
2 | 4
3 | 8
4 | 16
5 | 32
6 | 64
7 | 128
8 | 256
9 | 512
10 | 1024
Assuming 8-bit 2’s complement numbers.
X = 001001112
= 25+22+21+20 = 32+4+2+1
= 3910
X = 111001102
-X = 00011010
= 24+23+21 = 16+8+2
= 2610
X = -2610

## Slide 26: Converting Decimal to Binary (2’s C)
First Method: Division
Find magnitude of decimal number. (Always positive.)
Divide by two – remainder is least significant bit.
Keep dividing by two until answer is zero, writing remainders from right to left.
Append a zero as the MS bit; if original number was negative, take two’s complement.
X = 104ten 104/2 = 52 r0 bit 0
52/2 = 26 r0 bit 1
26/2 = 13 r0 bit 2
13/2 = 6 r1 bit 3
6/2 = 3 r0 bit 4
3/2 = 1 r1 bit 5
X = 01101000two 1/2 = 0 r1 bit 6